## Slide 1
Solar Carport Feasibility Analysis
27424 Pine Valley Dr | Evergreen, CO 80439 | 7,500 ft Elevation
Solar Carport vs. Non-Solar Carport | Technical & Economic Assessment
February 2026

## Slide 2
The Key Insight
Non-Solar Carport
$8,350
Total cost with zero financial return
Covered parking only
Payback: Never
Solar Carport
$20,550
Solar premium over non-solar: $12,200
Generates $995 - $1,495/yr in electricity value
Covered parking + energy production
Premium Payback: 8 - 12 years

## Slide 3
Site Conditions: Evergreen, CO
60 PSF
Snow Load
Ground snow load per ASCE 7-10. Exceeds most residential carport ratings.
110 MPH
Wind Speed
3-second gust design. Exposure B, Risk Cat II. Narrows structure options.
36"
Frost Depth
Rocky decomposed granite. Drilled piers required. No standard post holes.
7,500 ft
Elevation
Extreme cold (-13°F), UV degradation, altitude derating on equipment.

## Slide 4
Structure Options
 | ChikoUSA Maximo 185 | MT Solar Custom | DPW MPM-G2 | Non-Solar Carport
Wind Rating | 185 MPH | Custom to site | 115 MPH | 90-120 MPH
Snow Rating | 60 PSF | Custom to site | 15 PSF | 30-40 PSF
Meets Reqs? | YES | YES | NO - DISQUALIFIED | VERIFY
Tilt | 5° fixed | 5-30° adjustable | 20° seasonal | Flat
Total Cost | $6,950-$7,550 | $12,000-$16,000 | N/A | $3,500-$6,200
Warranty | 10yr / 25yr life | 10-20yr | 10yr | 5-10yr
Verdict | RECOMMENDED | Premium option | DISQUALIFIED | Baseline

## Slide 5
Cost Breakdown: Solar vs Non-Solar
Line Item | Solar Carport | Non-Solar Carport | Solar Premium
Structure + freight + bolts | $8,900 | $5,300 | $3,600
Foundation (DIY) | $2,150 | $2,150 | $0
PE Engineering | $2,250 | $500 | $1,750
Panels (18x 440W) | $1,800 | $0 | $1,800
Microinverters + Gateway | $3,450 | $0 | $3,450
Electrical (wire/conduit/trench) | $1,150 | $0 | $1,150
Permits | $600 | $300 | $300
Miscellaneous | $250 | $100 | $150
TOTAL | $20,550 | $8,350 | $12,200
Shared costs (foundation, permits) | $2,750 | $2,750 | $0
Federal ITC (Sec 25D) | EXPIRED 12/31/2025 |  | 

## Slide 6
Payback Analysis
Full Cost Basis ($20,550)
20.7 years
Exceeds component useful life
Solar Premium Only ($12,200)
8.2 years
With TOU optimization + battery arbitrage $1,495/yr annual value
All Scenarios
Scenario | $/yr | Payback
Full cost, TOU | $995 | 20.7 yr
Full cost, Flat rate | $964 | 21.3 yr
Premium, TOU | $995 | 12.3 yr
Premium, Flat rate | $964 | 12.7 yr
Premium, TOU + optim. | $1,495 | 8.2 yr

## Slide 7
Interconnection: Line-Side Tap (Recommended)
System Architecture
Carport Array 18x IQ8A / 7.92 kW
→
Service Entrance (Line-Side Tap)
→
Grid
Main Panel
↓
Magnum MS4024PAE + EG4 Battery + Roof Array (3.6 kW)
→
Critical Loads Subpanel (Backup capable)
Why Line-Side Tap?
No passthrough conflict
Carport bypasses Magnum entirely. 42.5A combined > 30A limit solved.
Simplest, cheapest
Fused disconnect only ($0-200). Most inspector-friendly option.
Resilience trade-off
Carport is dead during outages. Roof array + battery still works.
Future-proof
Add IQ System Controller later ($1,500-2,000) if needed.

## Slide 8
TOU Optimization: Free Money (No Capital Required)
Immediate Annual Savings
$350 - $500
Available today, no carport needed
Action | Savings/yr | Cost
EV charging timer (after 9 PM) | $100-200 | $30-50
Battery arbitrage (Magnum program) | $530 | $0
Hot tub pre-heat before 5 PM | $50-100 | $0
Thermostat pre-conditioning | $50-100 | $0
Battery Arbitrage: How It Works
Charge battery from solar/grid during off-peak (6.8 - 7.9¢/kWh)
Discharge during on-peak 5-9 PM (18.3 - 21.3¢/kWh)
Spread: 11.5 - 13.4¢/kWh × 12 kWh/day = $1.38-1.61/day
Annual Breakdown
Summer (122 days): $196
Winter (243 days): $335
Total: $531/year

## Slide 9
Recommendation
BUILD THE SOLAR CARPORT
Configuration
ChikoUSA Maximo 185
18x 440W panels (new)
18x IQ8A microinverters (new)
5° fixed tilt, south-facing
Line-side tap interconnection
Underground conduit
DIY foundation + installation
Economics
Total cost: $20,550
Non-solar baseline: $8,350
Solar premium: $12,200
Annual value: $995-$1,495
Premium payback: 8-12 years
25-year NPV: Positive @ 5%
Rate escalation improves yearly
Next Steps
1. Implement TOU optimization NOW
2. Call JeffCo Planning (303-271-8700)
3. Call ChikoUSA (1-800-948-5390)
4. Get foundation quotes
5. Order equipment
6. Engage CO PE engineer
7. Submit permits